# Communications
The board speaks two types of protocols: text and binary. The text protocol is intended for direct human interaction such as for testing. The binary protocol is intended for machine to machine communications.
The text protocol is in the CLI style. There is a series of commands. Each command takes certain parameters. One can get a list of supported commands by typing ? Followed by the Enter key in a terminal that is connected to the board.
The binary protocol is a simple request/response model. The base component is a message. A controlling device sends a message to the board and the board responds in turn with another message. Specific functionality within the board is addressable via call indexes. A call index is a unique eight bit value that identifies a function. A call index is sent as part of the request message and also as part of the response message.
# Physical Connection
# Software
115200 8N1
## Terminal

### LOGIC_CORE
# Binary Protocol
All multi-byte binary protocol types (for example integers) are sent down the wire with the MSB (Most Significant Byte) first. In other words, assuming a transmission of two words I1 and I2 , the receiving buffer will look like this:

Buffer index 0	Buffer index 1	Buffer index 2	Buffer index 3
I1 MSB	I1 LSB	I2 MSB	I2 LSB

NOTE: This is in contrast to the I2C protocol which sends data down the wire LSB (Least Significant Byte) first. This is a design feature and definitely not an oopsie.
The binary protocol is a simple request/response model. The controlling device sends a request and the board responds with a response.
## Request
The request message has three fields:
1. Binary message identifier (one byte)
2. Request payload length (one word)
3. Request payload (function specific)
### Binary message identifier
This is always 0x40 (ASCII @). Presence of this character indicates to the message parser on the board that the rest of the bytes are part of a binary message.
### Payload length
This is a single word value that indicates the length of the payload in bytes. Maximum payload length is 65536 bytes.
### Payload
Stream of bytes that are specific to the function.
Request Message
Binary message identifier					Request payload length MSB
BYTE 0					BYTE 1
7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0

0x40

Request payload length LSB					Request payload
BYTE 2					BYTE 3 ...
7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0

## Request Message Payload
The only standard part of the payload is the first byte which is expected to be the call index. All remaining bytes are function specific.

## Continued on next page
## Response
The response message is very similar to the request message. The response message has the following fields:
1. Binary message identifier (one byte)
2. Call index (one byte)
3. Result code (one byte)
4. Response payload length (one word)
5. Response payload (function specific)
### Binary message identifier
This is always character 0x10.
### Call index
The call index that this message is in response to. This will be the same call index as in the request message.
### Result code
Function specific result code. The only standard codes are one and zero; one is success and zero is failure.
### Response payload length
Single word that indicates the length of the response payload.
### Response payload
Unlike the request payload there is no structure. The response data is function specific.

## Continued on next page
Response Message
Binary message identifier					Call index
BYTE 0					BYTE 1
7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0

0x10					Same as the call index in request

Result code. 1 == success					Response payload length MSB
BYTE 2					BYTE 3
7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0

Response payload length LSB					First byte of payload
BYTE 4					BYTE 5
7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0

NOTE: The binary message identifier is different between the request and response messages.
# Binary commands
## 0x00 – Reset board

## 0x01 – Get analog input values

## 0x02 – Get digital output status

## 0x03 – Set digital output status

## 0x04 – Get PMIC status

## 0x05 – Set PMIC status

## 0x06 – Get L1 calibration offsets

## 0x07 – Get L2 calibration offsets

## 0x08 – Set L1 calibration offsets

## 0x09 – Set L2 calibration offsets

## 0x0A – Get boot count

BYTE 0					BYTE 1
7	6	5	4	3	2	1	0	7	6	5	4	3	2	1	0

# Text Protocol
## STATUS
### I2C
### AI
### DO
### PMIC
### B
### C
## SET
### DO
### PMIC

## COMMAND
### V
### VS
### E
## PING
## RESET
## ?